## Slide 1: Content-Centric Networking (CCNx) @ Information Centric Networking RG (ICNRG)
RFC 8569: Content-Centric Networking (CCNx) Semantics
M. Mosko, I. Solis, C. Wood, July 2019
RFC 8609: Content-Centric Networking (CCNx) Messages in TLV Format
M. Mosko, I. Solis, C. Wood, July 2019
Information Centric Networking (ICN) is a shift from host-based networking using endpoint addresses to named content. CCNx, first announced in 2009, and revised in 2014, uses a combination of URI-like path names and hash names to fetch content secured via publisher signatures.

## Slide 2: Example Use Case
Interest
/example.com/photo.manifest,
keyed=0x4423…
CCNx
Network
Content Object
/example.com/photo. manifest,
Locators=/storage/sfo, /storage/nyc
Signature (keyed=0x4423…)
Interest
/storage/sfo, hash=0x7289…
/storage/nyc, hash=0xa3b1…
…
Content Object
Payload 0x7289…
Payload 0xa3b1…
CCNx Network
Consumer
Publisher
Or Cache

## Slide 3: Implementations
Community ICN (CICN)
  Linux Foundation (https://wiki.fd.io/view/Cicn)
  Vector Packet Processing (VPP), Socket-like I/O, Qt/QML video player
CCN-Lite
  University of Basel (http://ccn-lite.net)
  User space, Linux kernel, OMNeT++, Android, Arduino (Uno and AtMega328, 2 KiB RAM), RFduino (32 KiB RAM), RIOT, and Docker
Cefore
  NICT (National Research Institute in Japan) (https://cefore.net)
  Lightweight & extensible with a simulator and emulator.
Hybrid ICN
  Linux Foundation (https://wiki.fd.io/view/HICN)
  CICN integrated with IPv6 forwarding – beyond an overlay
  High-performance mobile video tests at large US carrier
  Internet Area WG: https://datatracker.ietf.org/doc/draft-muscariello-intarea-hicn